# Module TM1638
Ce module permet l’affichage de 8 caractères, il comporte en plus 8 leds et 8 boutons. L’interface est i2c.
On le trouve pour moins de deux euros sur Ebay
## Bibliothèque
https://github.com/rjbatista/tm1638-library
## Exemple :
#include <TM1638.h>

// definit un module avec
// data broche 8
// clock broche 7
// strobe broche 6
TM1638 module(8,7,6);

void setup()
{
  module.setupDisplay(true, 0);
  module.setLEDs(0);
  module.clearDisplay();
  module.setDisplayToString("DEMO 123");
}

void loop()
{
  byte keys = module.getButtons();
  module.setLEDs(keys);
}
## Procédures et fonctions

Instantiate a tm1638 module specifying the display state, the starting intensity (0-7) data, clock and stobe pins.

TM1638(byte dataPin, byte clockPin, byte strobePin,
       boolean activateDisplay = true, byte intensity = 7);

Set the display to a unsigned hexadecimal number (with or without leading zeros)

void setDisplayToHexNumber(unsigned long number, byte dots,
        boolean leadingZeros = true,
        const byte numberFont[] = NUMBER_FONT);

Set the display to a unsigned decimal number (with or without leading zeros)

void setDisplayToDecNumber(unsigned long number, byte dots,
        boolean leadingZeros = true,
        const byte numberFont[] = NUMBER_FONT);

Set the display to a signed decimal number (with or without leading zeros)

void setDisplayToSignedDecNumber(signed long number, byte dots,
        boolean leadingZeros = true,
        const byte numberFont[] = NUMBER_FONT);

Set the display to a unsigned binary number

void setDisplayToBinNumber(byte number, byte dots,
        const byte numberFont[] = NUMBER_FONT);

Set the LED at pos to color (TM1638_COLOR_RED, TM1638_COLOR_GREEN or both)

virtual void setLED(byte color, byte pos);

Set the LEDs. MSB byte for the green LEDs, LSB for the red LEDs

void setLEDs(word led);

Returns the pressed buttons as a bit set (left to right).

virtual byte getButtons();

Set the display (segments and LEDs) active or off and intensity (range from 0-7).

virtual void setupDisplay(boolean active, byte intensity);

Set a single display at pos (starting at 0) to a digit (left to right)

virtual void setDisplayDigit(byte digit, byte pos, boolean dot,
        const byte numberFont[] = NUMBER_FONT);

Set the display to an error message

virtual void setDisplayToError();

Clear a single display at pos (starting at 0, left to right)

void clearDisplayDigit(byte pos, boolean dot);

Set the display to the values (left to right)

virtual void setDisplay(const byte values[], unsigned int length = 8);

Clear the display

virtual void clearDisplay();

Set the display to the string (defaults to built in font)

virtual void setDisplayToString(const char* string, const word dots = 0,
        const byte pos = 0,
        const byte font[] = FONT_DEFAULT);

Set the display to the String (defaults to built in font)

virtual void setDisplayToString(String string, const word dots = 0,
        const byte pos = 0,
        const byte font[] = FONT_DEFAULT);